## Slide 1: Toward Timeout-less Transport in Commodity Datacenter Networks
Hwijoon Lim (KAIST), Wei Bai (Microsoft Research), Yibo Zhu (ByteDance), Youngmok Jung (KAIST), Dongsu Han (KAIST)

## Slide 2: Packet Drops in Datacenter Networks
In datacenter networks, we still suffer from packet drops.
Shallow Buffer
5.12kB per port per Gbps*
tree structure by SBTS from the Noun Project
Graph by Wuppdidu from the Noun Project
tortoise by HeadsOfBirds from the Noun Project
Reactive Congestion Controls
1 RTT tens of
Some packet drops cannot be detected in a timely manner.
* Bai et al (2017) ** Zhang et al (2017)
Chart: 
| 1 | 10 | 40 | 100
 | 80 | 19.2 | 9.6 | 5.12
Utilization
Microbursts
90% of duration < 200 **

## Slide 3: Impact of Timeouts
RTO
(Retransmission Timeout)
Sender
Receiver
…
#1
#2
#3
#3
Data packet
ACK packet
Packet drop
ACK
ACK
ACK
Timeout
< 100 us
> 4 ms
RTT
(Round Trip Time)
>>
Tens of
Few ms

## Slide 4: Can we use aggressive timeouts?
In TCP, RTO is calculated as
Can we just reduce RTOmin to a lower value? (200us)*
Reducing RTOmin may not be enough because RTT variation is very large.
* Vijay Vasudevan et al (2009)
Chart: Time (ms)
Chart: Time (ms)
CDF
CDF
Background Flows
Foreground Incast Flows
RTOmin
RTOmin

## Slide 5: Can we use aggressive timeouts?
Can we use aggressive static timeout (fixed RTO)?
Aggressive RTO degrades throughput due to spurious retransmissions.
Chart: 
| Baseline | Fixed
Foreground 99%-ile | 9.0368 | 5.2922
Chart: 
| Baseline | Fixed
Background Average | 29.9896 | 63.9422
Background
Average FCT
Chart: 
| Baseline | Fixed
Timeout | 89766 | 4566591
Foreground
99%-ile FCT
# of Timeouts
ms
ms
Million
51x
2.1x
May cause undesirable interactions with network diagnosis*
* Azrani et al (2016)

## Slide 6: Existing Solutions to Mitigate Side Effect of Loss
Improve Loss Recovery
  TLP (Tail Loss Probe) [SIGCOMM '13]
  IRN (Improved RoCE NIC) [SIGCOMM '18]
Lossless Network
  PFC (Priority-based Flow Control)
Novel Switch Support
  NDP [SIGCOMM '17]
  CP (Cut Payload) [NSDI ’14]
  FastLane [SoCC ’15]
Protocol specific, Ineffective
Switch ASIC modification
Many Side effects

## Slide 7: Existing Solutions to Mitigate Side Effect of Loss
Improve Loss Recovery
  TLP (Tail Loss Probe) [SIGCOMM '13]
  IRN (Improved RoCE NIC) [SIGCOMM '18]
Lossless Network
  PFC (Priority-based Flow Control)
Novel Switch Support
  NDP [SIGCOMM '17]
  CP (Cut Payload) [NSDI ’14]
  FastLane [SoCC ’15]
Protocol specific, Ineffective
Switch ASIC modification
Many Side effects
Can we minimize the impact of packet loss in a general and deployment-friendly way?

## Slide 8: Existing Solutions to Mitigate Side Effect of Loss
Improve Loss Recovery
  TLP (Tail Loss Probe) [SIGCOMM '13]
  IRN (Improved RoCE NIC) [SIGCOMM '18]
Lossless Network
  PFC (Priority-based Flow Control)
Novel Switch Support
  NDP [SIGCOMM '17]
  CP (Cut Payload) [NSDI ’14]
  FastLane [SoCC ’15]
Protocol specific, Ineffective
Switch ASIC modification
Many Side effects
TLT (TimeoutLess Transport)
  Building block for various transport protocols
  Readily deployable using commodity switches
Can we minimize the impact of packet loss in a general and deployment-friendly way?

## Slide 9: TLT: Key Observation
Not all packet drops have the same impact!
Sender
Receiver
…
#1
#2
#3
#3
Data packet
ACK packet
Packet drop
ACK 2
ACK 3
ACK 4
Timeout
Sender
Receiver
#1
#2
#3
#2
ACK 2
ACK 2
ACK 4
Timeout
No Timeout

## Slide 10: TLT Design

## Slide 11: TLT Design Overview
Sender
Receiver
(1) Important Packet Selection at Hosts
Switch
Important Packet
Unimportant Packet
We mark some packets as important and keep them lossless inside the network.

## Slide 12: TLT Design Overview
Sender
Threshold = 5
Switch
(2) Selective Dropping at Switches
Receiver
Important packets remain lossless inside the network.
Important Packet
Unimportant Packet

## Slide 13: TLT: Key Challenges
  Which packet should be marked as important?
    Which packet loss may trigger timeout?
    # of important packets should be minimal
  How to selectively drop the unimportant packet?
    Queue separation would cause severe out-of-order problem.
    How can we differentiate unimportant packet inside the same queue?

## Slide 14: TLT Design: Important Packet Selection at Hosts
Example: RDMA (DCQCN)
Control how fast the packet is injected to the network
Timer triggers new packet transmission
Window-based Transport
Rate-based Transport
Example: TCP, DCTCP, HPCC, IRN
Control the number of inflight packets under the window limit
ACK triggers new packet transmission

## Slide 15: TLT Design: Important Packet Selection at Hosts
Common Rule: Mark all control packets important
Sender
Receiver
…
#1
ACK Loss
#2
ACK
#2
ACK
ACK
Sender
Receiver
#1
#2
ACK
ACK

## Slide 16: TLT Design: Important Packet Selection at Hosts
Example: RDMA (DCQCN)
Control how fast the packet is injected to the network
Timer triggers new packet transmission
Window-based Transport
Rate-based Transport
Example: TCP, DCTCP, HPCC, IRN
Control the number of inflight packets under the window limit
ACK triggers new packet transmission

## Slide 17: Challenge of Window-based Transport
Maintaining self-clocking is critical
Sender
Receiver
…
#1
#2
#3
#3
Data packet
ACK packet
Packet drop
ACK
ACK
ACK
Timeout

## Slide 18: Key Idea of Important Packet Selection (Window-based)
Always keep one in-flight important data packet
Sender
Receiver
Important Data
Important Echo
Important Data
Important Echo
Data packet (Unimportant)
Data packet (Important Data)
ACK packet
ACK packet (Important Echo)
Lossless

## Slide 19: Important Data Packet Preserves Self-clocking
#3
Guaranteed fast loss detection
Sender
Receiver
Important Data
Important Echo
Can’t tell whether unimportant data packet is lost yet
ACK
#1
#2

## Slide 20: Important Data Packet Preserves Self-clocking
Guaranteed fast loss detection
Sender
Receiver
Important Data
Important Echo
Guaranteed timely loss detection
Important Data
Important Echo
ACK
ACK
#1
#2
#3
#4

## Slide 21: Important Data Packet Preserves Self-clocking
Guaranteed fast loss detection
Sender
Receiver
Important Data
Important Data
Important Echo
Important Echo is a reliable indicator for loss detection.
Can tell whether lost
Important Echo
ACK
ACK

## Slide 22: Preserving one in-flight important data packet
What if the base transport does not allow further transmission when the sender receives an important echo?
Sender
Receiver
Important Data
Important Echo
Failed to preserve one in-flight important data packet
To keep important ACK-clocking, retransmit a part of packet by marking as important.
Not enough window or no new data

## Slide 23: Preserving one in-flight important data packet
Retransmit packet proactively (unACKed and previously sent as unimportant)
Sender
Receiver
Important Data
Important Echo
#1
#2
#2
Retransmit
Adaptively change the size of retransmitted packet to minimize impact

## Slide 24: TLT Design: Important Packet Selection at Hosts
Example: RDMA (DCQCN)
Control how fast the packet is injected to the network
Timer triggers new packet transmission
Window-based Transport
Rate-based Transport
Example: TCP, DCTCP, HPCC, IRN
Control the number of inflight packets under the window limit
ACK triggers new packet transmission

## Slide 25: Challenge of Rate-based Transport
No ACK-clocking on rate-based transport. Timeout only happens …
Sender
Receiver
…
#97
At the end of the message
Sender
Receiver
…
First retransmitted sequence gets lost
#10
ACK
ACK
ACK
…
ACK
#98
#99
#99
…
#10
ACK
NACK 10
NACK 10
#11
(Retx.) #11
#12
(Retx.) #10
(Retx.) #12
NACK 10
NACK 10
…
…

## Slide 26: Key Idea of Important Packet Selection (Rate-based)
1. Mark the last packet of the flow as important
Sender
Receiver
…
#97
ACK
ACK
…
ACK
#98
#99
#99
(Optional) can mark every N packet as important for timely loss detection
Sender
Receiver
…
#97
ACK
ACK
#98
#99
NACK
ACK
#98

## Slide 27: Important Packet Selection at Hosts (Rate-based)
Sender
Receiver
…
…
#10
ACK
NACK
NACK
#11
(Retx.) #11
#12
(Retx.) #10
(Retx.) #12
ACK
ACK
…
…
Sender
Receiver
…
#10
…
#10
ACK
NACK 10
NACK 10
#11
(Retx.) #11
#12
(Retx.) #10
(Retx.) #12
NACK 10
NACK 10
…
…
ACK
2. Mark the first packet during the retransmission as important

## Slide 28: TLT Design: Selective Dropping at Switches
Limit the queue buildup of unimportant packets by color-aware dropping
Red Threshold = 3
Switch Egress Queue
Proactive Drop
ACL Table
DSCP | Color
Important | Green
Unimportant | Red
Packet Ingress

## Slide 29: Choosing Color-aware Dropping Threshold
DCTCP
DCQCN
Threshold should be ≥ max queue length of steady state for the base transport
Queue Length
Time
Queue Length
Time

## Slide 30: Evaluation

## Slide 31: Evaluation Setup
Testbed Setup
  Implement prototype of TLT on Mellanox Messaging Accelerator (VMA)
  9 hosts with 40Gbps NIC connected to a single switch (Broadcom Tomahawk)
  Microbenchmark + Evaluate application performance (TCP, DCTCP)
Simulation Setup
  Simulated TCP, DCTCP, DCQCN, IRN, HPCC on NS-3
  96-host leaf-spine topology (40Gbps Link Capacity)
  Evaluate realistic workloads (web search)

## Slide 32: Testbed Experiments – Incast
TLT reduces tail FCTs up to 97.2% by effectively eliminating timeouts.
Chart: Number of Flows
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190 | 195 | 200
Kernel | 169.4441 | 217.9357 | 179.8685 | 229.7095 | 327.6712 | 351.8837 | 382.2744 | 448.5857 | 424.5537 | 410.4699 | 468.0316 | 530.5797 | 566.1103 | 633.5859 | 726.0082 | 654.4502 | 777.5487 | 758.5324 | 4151.6314 | 4306.1507 | 12311.8998 | 997.0859 | 63175.0279 | 17033.4741 | 67293.9542 | 50049.8289 | 5272.6407 | 38239.4979 | 40768.9522 | 17006.5348 | 9573.1343 | 38087.3621 | 22821.1424 | 26799.4397 | 112978.8506 | 1373.4489 | 73408.5529 | 21161.7102 | 5678.4129 | 66089.2386
VMA | 89.514 | 153.5657 | 213.9233 | 282.5682 | 338.1422 | 401.9821 | 412.1765 | 495.3726 | 23161.6885 | 33485.1012 | 32474.7528 | 32101.47 | 30325.3919 | 34095.5689 | 29672.9901 | 29802.9318 | 29854.5838 | 29959.8288 | 29090.5918 | 27518.6624 | 25913.8336 | 27699.8 | 28479.5534 | 27118.4487 | 27051.7252 | 25635.7565 | 28169.5372 | 26060.6856 | 26960.361 | 26838.3284 | 26586.0696 | 28195.5649 | 26783.8239 | 24873.73 | 25590.5152 | 25733.8779 | 26448.9042 | 27640.5021 | 26698.5986 | 27338.6743
VMA+200us minRTO | 87.8289 | 148.3566 | 218.2111 | 270.2515 | 325.682 | 378.6497 | 426.5207 | 484.8385 | 10590.6292 | 37754.093 | 37842.73 | 40030.5544 | 36563.2422 | 36408.2624 | 36055.7995 | 32218.0423 | 29493.8152 | 31946.2163 | 29657.0129 | 29355.4873 | 29319.5426 | 18656.0596 | 25068.03 | 27701.2271 | 27322.7683 | 28650.5185 | 28603.3206 | 22620.901 | 28920.7553 | 31145.721 | 30371.3465 | 24051.0448 | 29391.3221 | 24033.3361 | 31644.866 | 31055.5846 | 21569.7956 | 23660.9073 | 29110.7261 | 30793.3272
VMA+TIRE | 86.6926 | 236.6223 | 305.2155 | 360.3614 | 431.4769 | 507.2027 | 573.984 | 687.8133 | 842.397 | 932.7969 | 1037.3502 | 1341.5402 | 1369.0459 | 1445.9229 | 1649.9329 | 1858.7488 | 1834.3013 | 1952.7572 | 2190.4548 | 2108.5391 | 2265.6545 | 2406.4938 | 2481.9641 | 2557.9249 | 2725.1522 | 2873.4807 | 2826.389 | 2978.5636 | 3204.4696 | 3234.6131 | 3250.9002 | 3392.3111 | 3670.5547 | 3577.8417 | 3782.871 | 3899.4556 | 3943.4737 | 4096.2276 | 4241.4457 | 4297.6752
Chart: FCT (ms)
Linux Kernel
VMA
VMA + 200us RTOmin
VMA+TLT
Tail FCT of DCTCP
CDF of FCT for DCTCP flows

## Slide 33: Testbed Experiments – Application Performance
TLT keeps variance in response time low by mitigating timeouts.
Chart: Number of Flows
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180
DCTCP | 213.4101 | 346.6913 | 508.8906 | 694.6521 | 879.7834 | 5365.2254 | 13595.3575 | 12289.9965 | 21575.0949 | 17074.5139 | 5561.5927 | 20169.2575 | 26224.6103 | 17507.6745 | 15200.8363 | 24807.2304 | 18124.356 | 20105.5334
DCTCP+TIRE | 212.5784 | 409.0764 | 597.2734 | 862.6962 | 1013.3963 | 1202.0539 | 1450.7782 | 1628.2826 | 1825.7449 | 2092.9364 | 2411.2479 | 2721.6882 | 2780.8898 | 3004.1044 | 3422.3571 | 3618.8871 | 3929.4974 | 4397.2744
HTTP Client
Redis
Node
NGINX Web Servers
Tail Response Time (DCTCP)
Testbed
Topology
DCTCP
DCTCP+TLT

## Slide 34: Large Scale Simulation – FCT (DCTCP)
TLT reduces the 99.9%-ile FCT of foreground incast flows by up to 81%.
Baseline
Baseline+TLP
Chart: 
| 12.975287038799998
Baseline | 19.3073
+TLP | 19.0447
200us minRTO | 20.5164
+TIRE | 22.7733
+PFC | 48.8276
+TIRE+PFC | 36.7481
Baseline+200us RTOmin
Baseline+TLT
Baseline+PFC
Baseline+PFC+TLT
Average Background (ms)
99.9%-ile Foreground (ms)
DCTCP
Better

## Slide 35: Large Scale Simulation – FCT (RDMA)
Chart: 
| 7.0863274722000273
Baseline | 1.3178
PFC | 1.5983
TIRE | 1.2417
PFCTIRE | 1.2566
TLT reduces the 99.9%-ile FCT of foreground incast flows by up to 69%.
Baseline
Baseline+TLT
Baseline+PFC
Baseline+PFC+TLT
Average Background (ms)
Average Background (ms)
HPCC
Better
DCQCN+IRN
DCQCN+SACK
Chart: 
| 3.3217340542000078
Baseline | 1.4487
TIRE | 1.363
Chart: 
| 1.614336493600026
PFCTIRE | 1.5935
Baseline | 1.6831
TIRE | 1.5596
PFC | 2.0053
99.9%-ile Foreground (ms)
99.9%-ile Foreground (ms)
99.9%-ile Foreground (ms)
Average Background (ms)
Better
Better

## Slide 36: Large Scale Simulation – Timeouts / PFC
Chart: 
| DCTCP
Baseline | 322.0571
+TLP | 168.0066
200us minRTO | 1191.1173
+TIRE | 0.091266
Chart: 
Baseline | 375.218 | 406.8478 | 393.7291
+TIRE | 0 | 0 | 0
# of Retransmission Timeouts
DCQCN
+IRN
HPCC
+SACK
DCQCN
+SACK
Baseline
Baseline+TLP
Baseline+200us RTOmin
Baseline+TLT
Baseline+PFC
Baseline+PFC+TLT
Chart: 
| DCTCP
+PFC | 29467.7001 | 5063.753 | 5719.7174 | 35351.0588
+PFC+TIRE | 21303.9631 | 1246.9957 | 943.6308 | 10877.4471
# of PFC PAUSE Frames
DCQCN
+IRN
HPCC
+SACK
DCQCN
+SACK
TLT virtually eliminates timeouts and greatly reduces the number of PFC PAUSE.
0
0
0
0.09

## Slide 37: Conclusion
TLT is a building block for existing datacenter transports to eliminate congestion timeouts.
TLT achieves timeoutlessness by making important packets lossless in the network.
Code: https://github.com/kaist-ina/ns3-tlt-tcp-public
Sender
Receiver
Switch